## Slide 1: Hydro Education HUB Introduction
Introduction to Hydro Energy
Renewable energy workshop
13.03.2024

## Slide 2: At the End of the Introduction, you will…
…Experience the importance of hydropower in Ghana
Explore how hydropower contributes to meeting Ghana's energy needs to power households.
…Understand the history and development of hydro energy
Learn how hydro energy evolved from ancient water wheels to modern hydroelectric dams.
…Discover the wide-ranging potential of hydro energy

## Slide 3: 01 Table of contents 02
Introduction
Hydro Energy through time. Its global influence and Ghana’s present impact
Concepts of Grids and DERs
Experience how Grids and Distributed Energy Resources are working
05
Basics of Hydro Energy
Finding and harnessing Hydro Energy in diverse environments
03
Water Wheel & Turbine Types
Understand how Water Wheels and advanced Hydro Turbines work
04
Experiments with a Pelton Turbine
Understand Torricelli's Law, the resistance in water path and experiment with a pelton turbine

## Slide 4: Introduction 01
Learn about the impacts of hydro energy

## Slide 5: Introduction
Can you name some uses of hydro energy?
When do you think humans first started using water as a source of energy? (Give an estimate.)
Does a hydro power plant require fuel to operate?
What parts are essential for a hydro power plant to work?
Have you ever seen a hydro power plant? What did it look like? (You can sketch if you'd like.)
Why is hydro energy important for Ghana? (already today?, in the future?)
Do you think there is much more Hydro Energy potential in Ghana?
Is hydro energy renewable? Why?
Does hydro energy produce greenhouse gas emissions?
Choose three questions from the list below and write or sketch a brief answer. Share your answers with the class afterwards.
5 minutes
Notes: Teacher Note: Get people in „participation“ mode quickly, check what they already know

## Slide 6: History of Hydro Energy
Hydro energy has been used for over 3,500 years, making it the oldest and biggest source of renewable energy.
Humankind built water wheels near rivers to use the power of flowing water.
For which practices did they use the power of flowing water?
They used it to…
… grind grains like wheat into flour
… pump water to help grow crops
… power saws for cutting wood
Scan the QR-Code to see a Water Wheel in action!
Notes: https://www.youtube.com/shorts/1p_GqS0o-88 -> put in moodlebox
https://en.wikipedia.org/wiki/Watermill

## Slide 7: Present and Future
Later, Hydro has been one of the major drivers for the electrification of the early 20th century, producing reliable electricity.
As Technologies are advancing, we can improve the power output event further.
Hydropower will play a pivotal role in the future as a key driver of sustainable energy, supporting global efforts to transition to cleaner power sources, stabilize energy grids, and combat climate change
Notes: https://ourworldindata.org/grapher/share-electricity-hydro?tab=charthttps://ourworldindata.org/grapher/share-electricity-hydro?tab=chart

## Slide 8: Examples
Akosombo Dam (Volta Dam), Ghana
1965 completed
1020 Megawatt
Estimate: How many households could be powered for 1 year?
Three Gorges Dam, China
2006 completed
Largest power station worldwide
22500 MW
Way over 1 million households!
Notes: https://commons.wikimedia.org/wiki/File:Akosombo_Dam_is_spilling_water,_Ghana.JPG

## Slide 9: Hydro Energy in Ghana
In 2020, Ghana's energy mix comprised 69% fossil fuels (mainly oil and gas) and 31% renewables.
With examples like the Akosombo or the Bui Dam, Hydropower has long been a cornerstone of Ghana's energy system.
It also supports irrigation projects in the surrounding areas.
Bui Dam
What percentage of the 31% renewable energy share can be attributed to hydropower?
Notes: Source: https://www.researchgate.net/figure/Existing-and-Potential-Hydro-Power-Sites-in-Ghana-6_fig2_360157751​ The role of renewable energies in sustainable development of Ghana​ https://www.sciencedirect.com/science/article/abs/pii/S030142152300352X

## Slide 10: Ghana’s – Energy Mix
Hydropower is a significant contributor to Ghana's energy supply, driving a large portion of the nation's electricity generation. Moreover, there is substantial untapped potential for expanding hydro energy production across the country!
Chart: 
| Oil & Gas | Hydro | Solar | Wind
Renewables | 69 | 29 | 1 | 1

## Slide 11: Unlock the World of Hydro Energy
Hydropower has vast untapped energy potential and has significantly impacted society by creating jobs, economic growth, and being a reliable source of renewable energy.
This is only the beginning—technological advancements and innovative approaches are paving the way for greater efficiency and output.
Let’s explore the manifold facets of harnessing the power of moving water in the dynamic world of hydropower!

## Slide 12: Basics of Hydro Energy 02
Learn about the water cycle and where hydro energy can be found?

## Slide 13: Where is Hydro power found?
Hydro Power Hunt Challenge!
In this activity, you will explore the map of Ghana and search for spots where hydro energy can be found!
You’ll also learn how geography plays a role in making Hydro Energy possible.
Find all the information on page 10 in your worksheet!

## Slide 14
Hint: In the introduction, you have seen examples of various hydroelectric power plants located in different regions and environments.
Task 1
On page 11 in your Worksheet you will find a map of Ghana.
Identify and mark potential locations where you think hydroelectric power plants could be built. Indicate these spots with red dots on your map.
Rank your possible locations from best to worst and have an argument for, and against it ready.
Discuss in your group what makes the location you choose suitable?
20 minutes
Notes: https://www.grida.no/resources/5306

## Slide 15: Definition - Hydro Energy
Definition of Hydro Energy
Hydro energy is a form of renewable energy derived from the movement of water.
It's typically harnessed by converting the kinetic or potential energy of flowing or falling water into mechanical energy and subsequently into electrical energy using turbines and generators.
The term "hydro" originates from the Greek word "hydor", which translates to water.
"Energy", in a scientific context, is defined as the capacity to perform work, measured in Joules (J). (as you might know from previous worksheets)

## Slide 16: Conversion of Flowing Water to Energy
Refresher Potential & Kinetic Energy.
Water at a high place possesses potential energy due to its ability to fall.
When it flows down due to gravity, the energy turns into kinetic energy (movement).
Machines like turbines (for example a water wheel) use this moving water to make electricity!
How is the water coming up the hill again? …

## Slide 17: … the water cycle
The natual water cycle makes hydro power a seemingly ever lasting renewable source of energy. 4 Stages:
Evaporation: water coming from oceans, lakes and rivers turn into vapor and rise into the atmosphere
Condensation: the water vapor cools and forms clouds
Precipitation: Rain / Snow is falling from the coulds – for example in the mountains
Collection: small droplets on the ground form a river and ist way downhill again.
The main driver of the water cycle is the sun!
Notes: https://www.swfwmd.state.fl.us/residents/education/h2o-zone/the-water-cycle

## Slide 18: Where is Hydro Energy found?
Form groups of 3-5​
Go to page 13 on your worksheet, where you will find Task 2.​
Complete the task using the provided word bank!
If you have any questions, do not hesitate to ask!
Read the summary afterwards
20 minutes
Notes: In the teachers worksheet it is p.14!

## Slide 19: Water Motion can be found in various Places
Notes: Pixabay free pictures https://www.clean-energy-ideas.com/hydro/tidal-power/what-is-tidal-power-tidal-energy-explained/

## Slide 20: Hydro Energy: Rivers
Why are Rivers Important?
Rivers are the primary source for Hydro-Energy
Due to their continuous water flow, they provide kinetic energy to spin turbines, converting it into electricity.
In theory, any river has the potential to support a dam, which can regulate its flow to provide consistent energy production.
Have you ever noticed if the river near your home has higher or lower water levels at different times of the year?
Team up with your seat neighbor and complete Task 1 on page 15
Notes: p.16 in teachers worksheet!

## Slide 21: Hydro Energy: Rivers
Managing a Semi-regulated River for Energy Production
Objective: Analyze a semi-regulated river for hydroelectric energy production under different scenarios. Predict outcomes, discuss challenges, and propose solutions to maintain energy production while managing other factors.
Start Scenario: A semi-regulated river flows through a hydroelectric power plant.
Normal production capacity: 30 MW under average water flow conditions.
Your Role:You work in a Hydro Power Plant near a river. Work individually or in small groups to analyze each scenario and try to answer all questions.
The Teacher is guiding you through the different Scenarios step-by-step!
Find all information on page 16 – Task 2-4 in your worksheet!
20 minutes
Notes: Teacher Note:
Students can either form groups and solve it in smaller groups (like presented)
Quicker: Read the description together and do it all together in class with teacher guidance
p.17 in teachers worksheet!

## Slide 22: Rivers - Variation
Comparison of wet and dry season river flow in the Great Ruaha River from two vantage points.
The Importance of Consistent River Flow
A stable and continuous river flow is crucial for maximizing energy production in hydroelectric systems.
Impact of Seasonal Changes:
Rainy Season: High water levels provide stronger flow, leading to increased turbine efficiency and energy output.
Dry Season: Reduced water flow decreases the energy production capacity, highlighting the need for careful management of water resources
Therefore, maintaining consistent water levels ensures the reliable operation of turbines and maximizes the potential of hydro energy systems.
Notes: Source of the iamge: Stears, K., Nuñez, T.A., Muse, E.A. et al. Spatial ecology of male hippopotamus in a changing watershed. Sci Rep 9, 15392 (2019). https://doi.org/10.1038/s41598-019-51845-y

## Slide 23: Hydro Energy: Oceans
Think about the ocean, like the Atlantic Ocean in Ghana.
Answer the following questions:
What natural forces create tides and waves?
Guess what is the largest tidal difference (highest and lowest water levels) found on Earth?
How might we use these natural forces, like tides and waves, to generate hydropower?
You can find all instructions in your Worksheet page 20
Collect your answers in your worksheet.
Afterwards, discuss in class and summarize on the blackboard!
Understanding Tides & Waves
15 minutes
Notes: Teacher Note: look at the sample solution notes and compare suitable answers given from students; then write a solution together (their answers + aid of sample solution)
p.21 in the teachers worksheet!

## Slide 24: Oceans: Tides and Waves Energy
Scan the QR-Codes and watch the animations and videos about Tidal (left) and Wave (right) Hydro Energy Systems!
Notes: https://www.youtube.com/watch?v=sLIHQ-2TbvA&ab_channel=TUDelft
https://www.youtube.com/watch?v=VkTRcTyDSyk&ab_channel=StudentEnergy
https://www.youtube.com/watch?v=8miWW2QyN_4&ab_channel=OurFuture.Energy
https://www.youtube.com/watch?v=F0mzrbfzUpM&ab_channel=GreenpeaceUK

## Slide 25: Oceans
Oceans
Covering more than 70% of Earth's surface, oceans hold
immense energy potential.
Renewable energy can be harnessed from:
Tides – Driven by the gravitational pull of the moon and sun.
Waves – Generated by wind moving across the ocean’s surface.
Ocean-based hydro-energy, particularly tidal systems, is a reliable and consistent power source
Harnessing the power of tides and waves for renewable energy.

## Slide 26: Oceans
Sources of Ocean Energy
Tidal Energy
Uses the rise and fall of tides to move turbines.
Works well in coastal regions with strong tidal ranges.
Wave Energy
Converts the up-and-down motion of waves into electricity.
Ideal in areas with consistent wave activity.
Tidal Energy System
Wave Energy System
Notes: Sources: https://education.nationalgeographic.org/resource/tidal-energy/

## Slide 27: Tidal and Wave Hydro Energy - Innovations
While the ocean has enormous potential for generating energy, harnessing this energy is challenging due to the unpredictability and harsh conditions of the sea
Despite the challenges, there is great potential for innovation in ocean energy. With the right advancements in technology, ocean energy could become a significant contributor to global renewable energy in the future.
Real Life Examples:
Pelamis Wave Energy Converter, Scotland
Sihwa Lake Tidal Power Station 240MW
Notes: https://www.researchgate.net/figure/Pelamis-wave-energy-converter-courtesy-Pelamis-wave-power_fig9_298424440 https://theenergyprofessor.com/what-is-tidal-power/

## Slide 28: Mountainous Regions
Debating Game – Worksheet
Form two equally sized groups
Turn to page 22 in your worksheet and read the instructions for the debating game carefully
Team GREEN Location 1: High up the mountain, meaning a steep incline.
Team BLUE Location 2: At the bottom of the mountain, meaning the incline is less steep.
Understanding Hydro Energy in Mountainous Environment
20 minutes
Notes: Note Teacher: Divide the classroom into two groups (e.g., down the middle) to speed up the group activity.
After the two groups have formed, display the next slide during the execution phase. Its page 24! in the Teachers Worksheet!

## Slide 29: Mountainous Regions
First: Discuss and Plan in your group!
Second: Prepare and Share: Be ready to present your findings afterwards in class!
Hint: Find arguments to support your location, focusing on the motion of water (for example: speed vs. volume) and how it could impact energy production.
20 minutes

## Slide 30: Waterfall Effect
Definition
The waterfall effect refers to the energy generated by water falling from a height.
This works because of gravitational potential energy converting into kinetic energy and then into mechanical or electrical energy.
In other words:
Water at the top of a hill (elevated) = Stored Energy (Potential Energy)
Imagine a rubber band: The higher you stretch it the faster it snaps back.
Falling Water = Energy in Motion: When the water starts falling, gravity pulls it down, turning that stored energy into motion.
Imagine you let go of the stretched rubber band.
Spinning the Water Wheel = Using the Motion: At the bottom, the fast-moving water spins a big wheel (turbine)
Notes: Note for the Teacher: if you see the blue Imagine an analogy/metaphor follows to explain the concept in other words (picturing),

## Slide 31: Waterfall Effect
The Waterfall Effect works for small systems like a water wheel, and large system like a huge hydroelectric dam in principle equally.
Look at the water wheel on the left:
Water coming from a river is directed towards the wheel.
The falling water pushes the paddles of the wheel, making it spin.
In Chapter 2 you will experience key factors influencing the fundamental principle of the Waterfall Effect!

## Slide 32: Waterfall Effect - Example
Scan the QR-Code and watch the Water Wheel in action!
Notes: https://www.youtube.com/shorts/2p_QU4iuV3A https://www.youtube.com/watch?v=0Y0A5yQO9eY&ab_channel=DayTooley

## Slide 33: Catchment Area & River Basins
Combine your previous knowledge about rivers, the waterfall effect and the water cycle!
Form groups of 3 to 5 and start!
Turn to page 25 of your Worksheet and start with Task 1
Share your answers and drawings afterwards in class
30 minutes
Notes: Teacher Note:
To speed up the exercise you could do ask the students to draw a catchment are and river basin at home and just provide the answer slide p.34/36 in class!
Ist p.27! in the teachers worksheet

## Slide 34: Catchement Area & River Basins
A catchment area is a smaller, more specific part of land where rainwater collects and flows into a single stream, river, or reservoir.
It’s focused on just one local water source, like a small stream or lake.
A river basin is much larger. It’s the entire area of land where all the water flows into one big river
It includes many smaller catchment areas that feed into streams, which then feed into the gib river (at the bottom)

## Slide 35: Catchment Area & River Basins
Now work through Task 2 and answer Questions 1-4 in your group
You can find Task 2 on page 26 in your Worksheet.
Share your answers and drawings afterwards in class
15 minutes
Notes: Teacher Note:
To speed up the exercise you could do ask the students to draw a catchment are and river basin at home and just provide the answer slide p.34/36 in class!
Its p.28 in the teachers worksheet

## Slide 36: Dams and Reservoirs
A dam is a big wall built across a river to stop or slow the flow of water.
This creates a lake behind it, called reservoir, where water is stored.
It collects water, especially in mountain areas where rivers flow from melting snow or rain.
The stored water can be released when needed, like saving energy in a battery.
Imagine A dam is like a faucet on a bathtub. It holds water in the tub (reservoir) and lets it flow out through the faucet at a controlled rate when needed.

## Slide 37: Challenge – Environmental Impacts Game
Scan the QR-Codes and watch the animations and videos of flooding of the 3-Gorges Dam in China
Afterwards, refer to page 28 on your Worksheet and conduct the Challenge about how water changes and affects its surroundings!
Notes: Teacher Note:
If you only have one setup: let students gather around the experiment setup and let a group of students carry out the tasks (rotating groups)
2. If you have multiple (at best 4) Setup's then divide the students groups to the 4 different scenarios. After they finished they can wander around the classroom and sketch the results of the environmental impact game
It is page 30 in the teachers worksheet
https://www.youtube.com/shorts/UD4rXnntirI https://www.youtube.com/watch?v=i-MPO8uEP8I&ab_channel=GoogleEarth https://www.youtube.com/shorts/uGXtzPGlFL4
https://www.youtube.com/watch?v=2LqOpbiwcaU&t=2s&ab_channel=BBCNews
https://www.youtube.com/watch?v=W_6bC5jiP5U&ab_channel=AlJazeeraEnglish

## Slide 38: Environmental Concerns - Silting
Silting
Concern: Dams trap sediment (dirt & sand) that would normally flow downstream.
  This sediment can reduce the capacitiy of the reservoir and affect water quality
Impact: The lack of sediment downstream can reduce soil fertility for agriculture and harm ecosystems that depend on the natural flow of nutrients.
Imagine a bathtub full of water. If you pour a little sand into it every day, eventually, the water level in the tub will rise because of the sand. In rivers, this happens slowly, and the riverbed becomes higher, which can make it harder for water to flow smoothly

## Slide 39: Environmental Concerns - Obstruction
Waterway Obstruction
Concern: Dams block the natural flow of rivers, preventing fish and other aquatic animals from migrating to spawn or move to different areas.
Impact: This obstruction can harm fish populations (like salmon), disrupt ecosystems, and reduce biodiversity in both the river and the surrounding areas.
Imagine a water slide at a pool. If something is blocking the water stream going down the slide, the water will have trouble flowing down smoothly. The water might even get stuck!

## Slide 40: Environmental Concerns - Flooding
Flooding
Concern: Building a dam often causes large areas upstream to be flooded,
  This can negatively influence ecosystems.
  When there is too much water in the reservoir, all channels must be opened to release the pressure. As a result, flooding can also occur downstream.
Impact: Flooding can displace local communities, drown wildlife habitats, and disrupt the natural balance of the surrounding environment, leading to long-term ecological damage.
Imagine you have a sponge soaked with water. If you keep adding water to the sponge, it eventually can’t hold any more, and the water starts to spill out. In the same way, if a river gets “too full”, the water will spill out onto the land, causing flooding.

## Slide 41: Every question you ask is a step towards knowledge

## Slide 42: Turbine Types in Hydro Energy 03
Build your own Water Wheel, learn how to operate it efficiently and experiment with different turbine types to understand how we can harvest hydro energy!

## Slide 43: Instructions – Build Your Own Water Wheel
Get your glue and scissors ready!
Please refer to the Worksheet Chapter 2 on page 38 for detailed instructions.
If there are not enough scissors or glue available, kindly assist each other by sharing and helping each other out!
If additional help is needed, do not hesitate to ask your teacher.
After constructing the water wheel, complete Tasks 1 and 2 on pages 41 and 42 of your worksheet.
You can work on them individually or in groups.
Notes: Teacher Note:
either do this Exercise as a whole class activity OR end the lecture here, give every student the task to craft 1 bucket and bring them to the next class. In the following class, y'all can assemble the full water wheel and start explaining
Its p.41 in the teachers worksheet!

## Slide 44: Why does a Water Wheel operate best for High-Volume and Low Head Height?
A water wheel operates efficiently with high-volume, low-head water flow because:
It relies on the weight and force of a steady stream of water rather than speed of the flowing water or height.
The large amount of water continuously fills the buckets, providing a stable and consistent power source.
Unlike some turbines, which depend on high-speed jets from tall falls, water wheels are designed to use slower-moving but larger quantities of water, making them ideal for wide rivers or streams with minimal height difference.

## Slide 45: Why does a Water Wheel operate best for High-Volume and Low Head Height?
Imagine you have a big spoon and want to scoop up lots of soup.
If someone pours the soup slowly but gives you a lot of it, your spoon stays full, and you can keep eating easily. But if they pour a little bit from really high up, most of the soup will splash everywhere, and your spoon won’t catch much.
The water wheel is like that spoon (bucket!) - it works best when there’s a big steady "pour" of water (high volume), even if it’s coming from close to the ground (low height).
Look at the waterfall on the left. Its easier to “catch” the water at the top, than at the bottom.

## Slide 46: Formula for Energy in Hydro Energy!?
In Class Challenge!
Work in groups of 3 - 5 and try to derive the formula for energy in words.
After 5 minutes, we will compare results and work together to derive the formula both in words and as a mathematical expression.
Hints Think about the water wheel tasks! What forces are required to make the wheel turn?
Key elements include the volume and height of the water.
20 minutes
Notes: Teacher Note:
To speed up this task you can also do this exercise as a guide in front of the class without having to form groups

## Slide 47: Formula for Energy - I
Imagine
If you drop the balloon from your hand, it makes a small splash because it doesn't fall far.
But if you're standing on top of a house and drop the balloon, it makes a much bigger splash, due to the greater height it falls from.
This shows that height is an important factor in determining the energy involved in the fall. The higher the drop, the more energy is released when the balloon hits the ground. This is equal to potential energy, which is the energy stored in water at a height before it falls, like into a water wheels buckets.

## Slide 48: Formula for Energy - II
Imagine
Holding a small balloon and a large balloon, both filled with water, and letting them fall from the top of a house.
The larger balloon will create a bigger splash because it has more water.
This shows that volume is the second key factor in determining the energy of moving water.
Next, think about gravity, the force that “pulls” everything, including water, towards the ground.
Gravity is essential for the movement of water in a water wheel.
Finally, we also need to consider density. What is density?

## Slide 49: Formula for Energy - III
What is density?
Imagine holding a cup of water and a cup of feathers.
The cup of water feels much heavier, even though both cups have the same volume.
This is because water is denser than feathers.
Density refers to how much mass is packed into a given volume. Since water has more mass in the same amount of space, it feels heavier compared to the feathers.
Can you now explain the Energy Formula in words?!
Solution
In Words: Energy = Density (p) * Volume (V) * Gravity (g) * Height (h)

## Slide 50: Formula for Energy – Hydro Power?
In Words: Energy = Density (p) * Volume (V) * Gravity (g) * Height (h)
m for mass: relates to the amount of water.
h for height: the higher the water is, the more potential energy it contains.
g for gravity: which pulls the water down, converting potential energy into kinetic energy (approximately 9.8 m/s2 on Earth)
p for density of water
Potential Energy = m * g * h
Mass can be written as Volume * Density of water: m = p * V
Insert m in the Potential Energy Equation = p * V * g * h
Energy = p * V * g * h
(you can also write: Total energy = potential energy + kinetic energy: Etotal = Epot + Ekin)

## Slide 51: Bevor we start with the Experiment
There are 3 major Turbine Types
Pelton
Kaplan
Francis
Scan the QR-Codes and watch the videos to familiarize yourself with the Experiments coming up next!
Notes: Short: Kaplan: https://www.youtube.com/shorts/WacPiUURB5g Francis: https://www.youtube.com/watch?v=qp3J1eRtKn0&ab_channel=ANDRITZGROUP Pelton: https://www.youtube.com/watch?v=f5gV2vRhCCY&ab_channel=LinquipCorporation Explanation of all 3 and an outlook of Operating Ranges: https://www.youtube.com/watch?v=k0BLOKEZ3KU&ab_channel=SabinsCivilEngineering

## Slide 52: Exercise – START!
Form Groups of 5 and help each other out in the team.
Do Tasks 1 to 4 following the instructions on your worksheet - Chapter 2 page 44.
If additional help is needed, do not hesitate to ask your teacher.
Notes: In the teachers worksheet ist p.46!

## Slide 53: Experiment - Discuss & Continue
Discuss with the whole class about your observations and findings.
Grande Dixence, Switzerland
Hoover Dam USA
Which Turbine Types are installed in the Hoover Dam (USA) and the Grande Dixence in Switzerland?
Hoover: Francis
Grande Dixence: Pelton

## Slide 54: Explanation: Why different Turbine Types?
The Kaplan, Francis, and Pelton turbines exist because water behaves differently in various environments, requiring specific turbine designs to harness its energy efficiently
Below, you can see three different shoe types that are suitable for different environments best. Which shoe do you think is the Francis, Pelton or Kaplan turbine and why?
Notes: Ask in class, then step by step unfold the analogy on the next slide!

## Slide 55: Explanation: Why different Turbine Types?
Kaplan Turbine: Ideal for large volumes of slower-moving water with low height differences, such as wide rivers.
Imagine: Kaplan turbines are like Flip-Flop’s – ideal for strolling in flat, areas. Their wide, flat design spreads weight over a larger area, allowing them to handle higher volumes without sinking into the sand.

## Slide 56: Explanation: Why different Turbine Types?
Francis Turbine: Best for environments with a balanced combination of flow rate and height, like medium-sized dams
Imagine: Francis turbines are like running shoes – versatile and effective for balanced conditions, whether running on a track or a trail, in flat and higher areas.

## Slide 57: Explanation: Why different Turbine Types?
Pelton Turbine: Designed for high water pressure and large height differences, such as tall mountain dams.
Imagine: Pelton turbines are like climbing boots – designed for extreme heights and steep conditions where maximum grip and targeted pressure is needed.

## Slide 58
Therefore, you can say:
These three turbine types perform better in different environments because they are optimized for specific water flow conditions (speed, volume, and pressure) to maximize energy generation.
Notes: https://www.daviddarling.info/encyclopedia/W/AE_water_turbine.html

## Slide 59: Hydro Education HUB Chapter 3
Factors Affecting Turbine Performance - Pelton Turbine Experiments
Renewable energy workshop
xx.xx.2024, xx

## Slide 60: What Impacts Turbine Output?
Turbine performance depends on
Velocity of water: Driven by head height and resistance
Water volume: Determines energy availability.
Turbine design: Blade type and rotor number.

## Slide 61: The Power of Height – Why It Matters
Height: Turning Potential Energy into Power
When water is stored at a higher level, it has potential energy because of gravity.
As the water falls, gravity converts this energy into kinetic energy (movement), which spins the turbine to generate electricity.
The higher the water, the more energy it carries! This is why dams are built tall, and water towers stand high.
High altitude dam
Low altitude dam
Notes: Teacher Note: the following text is an example of how to present the concept with an easy analogy “Imagine holding a ball at the top of a hill. If you let it go, it rolls down quickly, picking up speed. That’s potential energy turning into kinetic energy! Hydroelectric dams use the same principle with water—storing it high and letting it flow to power turbines.”

## Slide 62: Torricelli’s Law and Velocity of Water
How Does Velocity Affect Energy?
Torricelli’s Law: Water velocity increases with greater
where h = head height and g is the acceleration of gravity
To keep in mind:
Head Height: Taller water sources generate faster water jets and more energy.
Resistance: Obstacles in the water path reduce velocity, similar to resistance in electrical circuits.

## Slide 63: Now think
Would there be any difference between the cases present in the images?
What would be the speed of the water at the end of the fall of each of these?
Notes: Teacher Note: The “Now Think” section is designed to introduce discussion and debate between the students, some guidance questions are presented in this slide with the goal of trigger in class conversations

## Slide 64: Torricelli’s Law - Example
Scan the QR Code and let‘s watch Torricelli‘s law in action
Notes: https://www.youtube.com/shorts/2p_QU4iuV3A https://www.youtube.com/watch?v=0Y0A5yQO9eY&ab_channel=DayTooley

## Slide 65: Let’s do an experiment to learn about the relationship between volume and force

## Slide 66: Instructions
Get your materials ready, and refer to page 61 on the worksheet.
If you need support to clarify the experiment, scan the QR code and watch the video to get a better understanding.
If additional help is needed, do not hesitate to ask your teacher.

## Slide 67: From Water Tanks to Firefighters: Torricelli’s Law in Action
Water Towers: Have you ever seen tall water towers in cities or towns?
They store water at elevated heights. Torricelli’s Law explains why water flows rapidly from taps or hoses.
The greater the height of the water tank, the faster the water flows. This principle ensures consistent water pressure in homes.
Firefighter Hoses: When firefighters use hoses, the water comes out at high speed because it’s pressurised and sometimes elevated in tanks.
This speed helps them put out fires effectively.
The head height of water in fire trucks or towers gives the water its force, allowing it to reach far distances.

## Slide 68
How Water Volume Affects Power
  The amount of water (volume) determines how much energy it can transfer to turbines.
  More water = more energy to spin turbines
  Think of a big river during the rainy season—it flows faster and stronger, carrying more energy. That’s the power engineers capture to generate electricity.
Why Volume Matters – More Water, More Energy
Notes: Source of the iamge: https://education.nationalgeographic.org/resource/tidal-energy/ ; https://www.youtube.com/watch?v=8miWW2QyN_4

## Slide 69
How Does Resistance Affect Water Flow?
Water resistance (like rocks or narrow pipes) slows the water flow, reducing energy.
Similar to resistance in electrical circuits:
High resistance = low flow.
Low resistance = smooth, fast flow.
Imagine a river filled with rocks and logs—some areas flow quickly, while others slowly trickle. Just like water in pipes, resistance affects how smoothly turbines can harness water’s energy.
Smooth river flow
Obstructed river flow
Water Resistance – A River’s Journey

## Slide 70: Effect of resistance on water flow
Scan the QR Code, and let‘s watch an example of how obstacles can affect the water path and flow

## Slide 71: Let’s explore how obstacles (resistances) can affect the water flow with an experiment

## Slide 72: Instructions
Get your materials ready and refer to page 56 on the worksheet.
If additional help is needed, do not hesitate to ask your teacher.
Notes: Teacher note: As the experiment is completed, the “Now Think” section is designed to offer a discussion space between students. As a general recommendation, a question should be raised before introducing the analogy. An example could be “In which other scenarios, different to hydro energy, can we see obstacles affecting the flow?”

## Slide 73: Now think
In water flow, obstacles (like rocks or narrow paths) reduce the speed and distance the water can travel. In electric circuits, resistance slows the current, reducing energy flow.
Just as obstacles in a water path hinder flow, resistors in a circuit limit electric current.
Obstacles in water = Resistance in electricity.
Reduced water flow = Reduced electrical current.
Both systems show how resistance limits flow and efficiency.
Notes: Teacher note: As the experiment is completed, the “Now Think” section is designed to offer a discussion space between students. As a general recommendation, a question should be raised before introducing the analogy. An example could be “In which other scenarios, different to hydro energy, can we see obstacles affecting the flow?”

## Slide 74: Now let’s see the concepts we have discussed in action in a hydro energy turbine

## Slide 75: Water Testing Head Height and Energy Output
Let’s recap the most important information so we can see it clearly in action on the next experiment.
We will use a Pelton turbine.
What Are Pelton Blades? Curved buckets or blades designed to convert water’s kinetic energy into mechanical energy.
Why Blade Design Matters:
Shape: Curved to capture water’s force effectively.
Number: More blades ensure smoother rotation, but too many can create turbulence, reducing efficiency.
Optimized blade numbers and shapes are key for real-world turbine performance.

## Slide 76: Water Testing Head Height and Energy Output
Experiment Overview
What You’ll Test:
Observe how different head heights (80 cm, 130 cm, and 180 cm) impact energy generation and Understand the relationship between water pressure, turbine speed, and electricity output
Concept Recap
Higher head heights benefit turbines, but efficiency also depends on blade design and alignment:
Higher head height = Greater potential energy = Increased electricity generation.
Notes: Teacher Note: Here, the Hydro-Energy Kit is introduced, presenting some images of the kit, the step-by-step assembling instructions are on page 59 of the worksheet

## Slide 77: Instructions
Get your materials ready and refer to page 60 on the worksheet.
If additional help is needed, do not hesitate to ask your teacher.

## Slide 78: Now think
Imagine you are tasked with optimizing a hydroelectric power plant using a Pelton turbine. You have fixed the head height and valve position for maximum water flow efficiency.
Compare this setup with a photovoltaic (PV) system and a wind turbine.
What are the main differences in how these systems generate energy?
How external conditions (like sunlight, wind, or water flow) affect their performance?
Can you identify which system would be more reliable in a region with varying weather conditions and why?
Notes: Hydropower systems, like the Pelton turbine, rely on consistent water flow and controlled parameters such as head height and valve position to optimize energy generation, making them highly efficient in areas with stable water sources. In contrast, photovoltaic systems depend on sunlight availability, which varies with weather and time of day, while wind turbines rely on consistent wind speeds, which can be unpredictable. Among these, hydropower is often more reliable in regions with steady water flow, as it is less affected by weather variations, unlike PV systems that fail in cloudy conditions or wind turbines that become inefficient during calm periods.

## Slide 79: Concepts of Grid and Combining DERs 05
Understand the concept of a grid and the challenges it faces, as well as strategies to overcome them

## Slide 80: What Is a Grid, and Why Do We Need It?
The electricity grid is an interconnected system that delivers electricity from producers to consumers.
It connects power plants, transmission lines, and distribution systems to ensure efficient and reliable energy delivery
A grid also:
Enables sharing energy resources across regions, ensuring that areas with high demand or low generation can still meet their needs.
Balances fluctuations in renewable energy sources like wind and solar by pooling energy from more reliable sources such as hydro. Additionally,
Reduces energy waste by redistributing surplus power to where it’s needed.

## Slide 81: Predictability of Renewable Sources
One of the biggest challenges when thinking about renewable energies is reliability. These sources of energy depend on environmental factors that are unpredictable in the long term
Hydro Energy: Is highly predictable due to stable water flows, making it ideal for continuous and reliable energy generation. it is less affected by seasonal changes.
Photovoltaic (PV) Solar Energy: Solar energy is predictable on sunny days but limited to daylight hours. Cloud cover can reduce its output, highlighting its dependency on weather.
Wind Energy: Is the least predictable form of energy, as its output depends on weather conditions and geographic location. It can generate power day and night, but its variability poses challenges for grid stability.

## Slide 82
Combine your knowledge about PV, Wind, and Hydro Energy and their fluctuating behavior in energy production!
Turn to page 65 of your worksheet,
Read the instructions for Task 1
Follow the game to deepen your understanding of baseload and how different energy sources could rank in reliability of energy production.
Some Energy Sources are Better for Baseload!? – BINGO GAME
30 minutes
Notes: In the teachers worksheet its p.68!
FIND THE GAME GUIDANCE ON PAGE 70!!

## Slide 83: Reliability Order Renewable Energy Sources
Hydropower (Most Reliable)
Provides consistent and most controllable energy supply using for example stored water in reservoirs, making it ideal for baseload.
Photovoltaic (PV) Solar (Moderately Reliable)
Predictable during daylight hours with steady patterns based on day-night cycles. But no production during nighttime.
Wind Energy (Least Reliable)
Can generate power day and night if winds are steady, but highly variable.

## Slide 84: Baseload Requirements?!
Baseload Energy
The minimum level of power the grid needs to operate continuously, even during periods of low electricity demand.
Typically provided by power sources like coal, nuclear, or hydroelectric plants, which are able to operate 24/7.
Why is Baseload Important?
It ensures that critical services can run 24/7
For example: hospitals, streetlights, traffic systems and other essential infrastructure

## Slide 85: Electricity Generation = Demand!?
Combine your knowledge about PV, Wind, and Hydro Energy and their fluctuating behavior in energy production from the beginning of this Chapter!
Turn to page 68 of your worksheet,
Read the instructions
Follow the Energy Balancing Game to deepen your understanding of why electricity Generation must equal Demand in an Energy Grid and refresh your knowledge about different energy sources and their behavior.
45 minutes
Notes: In the teachers worksheet it is p.71!

## Slide 86: The Importance of Balancing Electricity Generation and Demand
The electricity grid operates on the principle that generation must! equal demand at all times.
Imbalances can cause:
          Over-generation: Leading to equipment damage or power surges.
  Under-generation: Resulting in blackouts or instability.
Why It Matters:
Constant adjustments are required to match fluctuating demand with generation.
Ensures system reliability, stability, and efficiency.

## Slide 87
Imagine a bathtub
Water entering via the shower head = electricity generation.
Water exiting through the drain = electricity demand.
Water inflow varies depending on varying electricity generation
Water outflow varies, based on numerous demand-side activities
If water enters faster than it exits (over-generation): The Bathtub overflows, representing grid overload and potential equipment damage.
If water exits faster than it enters (under-generation): The Bathtub empties, representing power outages or full blackouts.
Bathtub Example

## Slide 88: What are Buffers to keep Generation = Demand?
How It Relates to Electricity Grids:
A buffer system ensures the grid‘s stability – such as an additional water tank (Battery) near the bathtub.
In the Water Tank you can store excess electricity generation and release as needed, hence balance out the power grid.
Tools such as valves (controls) and reservoirs (batteries) help manage flow and balance.

## Slide 89: How Grids Handle Fluctuations
Buffers: Technologies like batteries store excess energy and release it during high-demand periods.
Demand Response Systems: These adjust electricity consumption patterns in real-time, aligning demand with available supply.
Peaker Plants: Operate during periods of high demand, quickly ramping up energy production to stabilise the grid.
By combining these mechanisms, grids ensure reliability and optimize the use of renewable energy, making the transition to sustainable energy sources feasible.
Renewable energy sources can be unpredictable, creating mismatches between generation and demand. Grids are essential in managing these fluctuations to maintain stability and.

## Slide 90: Why connecting energy sources makes sense
Now imagine the bathtub has multiple faucets (representing different energy sources like solar, wind, and hydro)
The solar faucet flows steadily during the day but stops at night.
The wind faucet is irregular, and flows based on wind conditions.
The hydro faucet provides a steady flow, acting as the most reliable faucet.

## Slide 91: Why connecting energy sources makes sense
By connecting all faucets to the bathtub, any variation in one faucet (energy source) can be compensated by another.
Balancing Inflows and Outflows
The bathtub drain (electricity demand) represents outflow, which depends on user activities like turning on lights.
When multiple faucets supply the bathtub, ensures:
No water shortages (blackouts).
No overflowing (energy waste or grid instability).
Multiple sources ensure a consistent water level in the bathtub, even if one faucet temporarily slows or stops.

## Slide 92: What are DERs and How They Interconnect?
Distributed Energy Resources (DERs): Small-scale energy generation units (e.g., solar panels, wind turbines, batteries) located close to where energy is used.
DERs are connected to the power grid, forming a decentralised system where energy can flow dynamically between sources and users. This interconnects the grid and the small-scale generators.
Interconnection Benefits:
Dynamic Flow: Energy flows between DERs and the grid, balancing supply and demand.
Resource Diversity: Combines various energy sources for steady supply even when one source is unavailable.
Localized Energy: Reduces transmission losses and increases efficiency.

## Slide 93: Batteries and Reliability in the Power Grid
Benefits of the integration of batteries:
Grid Stabilization: Smoothens energy fluctuations, reducing risks of overload or blackouts.
Integration with DERs: Complements renewables by storing energy from solar or wind during peak production for later use..
Batteries store excess energy during low demand and release it during peak demand, ensuring a constant energy supply.

## Slide 94: The Merit Order and Cost Optimization
Impact on Reliabilit, By prioritizing cost-effective resources, the grid maintains affordability while ensuring consistent energy supply.
Example: Due to their low cost, solar and wind are used during peak production, while batteries and peaker plants step in during shortfalls.
Merit Order is an economic principle that ranks energy sources by cost, ensuring the cheapest energy is used first

## Slide 95: 100,000
Did you know that an average human heart beats around these many times a day?

## Slide 96: Some interesting country studies
USA
New Guinea
DRC
National Human Genome Research
Climate Studies
Ebola Virus Disease

## Slide 97: The steps for a successful experiment
Plan your
experiment
What materials will you need? What steps will you follow?
Analyze results and draw conclusions
Look at the data you collected. Did it support your hypothesis?
02
04
Define the
hypothesis
Think about what you want to discover and guess the outcome
01
Conduct it and
collect data
Make sure to record all your observations and results
03

## Slide 98: Rubric
Criteria | Exceptional (4) | Proficient (3) | Basic (2) | Limited (1)
Scientific content | In-depth; accurate; interconnected | Solid; accurate; clear examples | Basic; somewhat accurate. Lacks depth | Limited; contains inaccuracies
Critical analysis | Well-structured; insightful; exceptional evaluation | Logically organized; thoughtful analysis; good critical thinking | Somewhat organized; lacks depth; basic critical thinking | Disorganized; minimal critical analysis
Clarity and focus | Clear; coherent; maintains focus with smooth transitions | Communicates clearly; generally smooth transitions | Somewhat clear; occasional lack of coherence | Unclear; disorganized; lacks coherence
Application of examples | Integrates varied, relevant examples effectively | Effectively uses examples for clarity and relevance | Includes some examples; limited in number or relevance | Lacks sufficient, relevant examples

## Slide 99: Short answer questions What is the scientific method, and why is it important in scientific research? Describe a natural phenomenon that captivates your curiosity. How would you approach investigating and explaining it scientifically? In what ways do scientific discoveries impact our daily lives?
The students should read the following questions and answer them in their paper. These questions require students to demonstrate their understanding of key concepts
01
02
03

## Slide 100: Group discussion
The wonders of space
Topics
Divide the class into small groups of 3-5 students. Assign each group a discussion topic or question. In their groups, they should discuss the topic and reach conclusions
Incredible world of microorganisms
Renewable energy sources
Genetics and heredity
Ecosystems and biodiversity
The scientific method in everyday life

## Slide 101: Essay
Select a topic for the essay. Students should research the topic, outline the structure and write a well-constructed essay
Topics
The interconnectedness of scientific disciplines: Choose two scientific fields and discuss how discoveries in one field can influence and contribute to advancements in another
The role of science in addressing global challenges: analyze the role of science in addressing global challenges. Choose one or more pressing issues and discuss how scientific advancements contribute to understanding, mitigating, or solving these challenges

## Slide 102: Conclusions
The process of conducting an experiment is crucial to understanding science. It helps students learn how to hypothesize, plan, execute, and analyze data in a systematic way
Visual representation of data can improve the understanding and interpretation of the results. It provides a clear way to present complex data sets and allows for easy comparisons
Knowledge about different materials is fundamental in science. This understanding can help students comprehend why certain materials are chosen for specific purposes
Scientific method
Data representation
Understanding materials

## Slide 103: Thanks!
Do you have any questions?
youremail@freepik.com |+34 654 321 432 | yourwebsite.com
Please keep this slide for attribution

## Slide 104: References

## Slide 105: Icon pack

## Slide 106: Alternative resources
Here’s an assortment of alternative resources whose style fits that of this template:
Electricity icon flat

## Slide 107: Resources
Did you like the resources used in this template? Get them on these websites:
Illustrations
Electricity icon flat set
Photos
Portrait female working
Male technician hand wearing gloves holding computer parts
Elevated view of electrical equipment and circuit board
Icons
Icon Pack: Electricity | Lineal

## Slide 108: Instructions for use
If you have a free account, in order to use this template, you must credit Slidesgo by keeping the Thanks slide. Please refer to the next slide to read the instructions for premium users.
As a Free user, you are allowed to:
Modify this template.
Use it for both personal and commercial projects.
You are not allowed to:
Sublicense, sell or rent any of Slidesgo Content (or a modified version of Slidesgo Content).
Distribute Slidesgo Content unless it has been expressly authorized by Slidesgo.
Include Slidesgo Content in an online or offline database or file.
Offer Slidesgo templates (or modified versions of Slidesgo templates) for download.
Acquire the copyright of Slidesgo Content.
For more information about editing slides, please read our FAQs or visit our blog:
https://slidesgo.com/faqs and https://slidesgo.com/slidesgo-school

## Slide 109: Instructions for use (premium users)
As a Premium user, you can use this template without attributing Slidesgo or keeping the "Thanks" slide.
You are allowed to:
Modify this template.
Use it for both personal and commercial purposes.
Hide or delete the “Thanks” slide and the mention to Slidesgo in the credits.
Share this template in an editable format with people who are not part of your team.
You are not allowed to:
Sublicense, sell or rent this Slidesgo Template (or a modified version of this Slidesgo Template).
Distribute this Slidesgo Template (or a modified version of this Slidesgo Template) or include it in a database or in any other product or service that offers downloadable images, icons or presentations that may be subject to distribution or resale.
Use any of the elements that are part of this Slidesgo Template in an isolated and separated way from this Template.
Register any of the elements that are part of this template as a trademark or logo, or register it as a work in an intellectual property registry or similar.
For more information about editing slides, please read our FAQs or visit our blog:
https://slidesgo.com/faqs and https://slidesgo.com/slidesgo-school

## Slide 110: Storyset
Create your Story with our illustrated concepts. Choose the style you like the most, edit its colors, pick the background and layers you want to show and bring them to life with the animator panel! It will boost your presentation. Check out how it works.
Pana
Amico
Bro
Rafiki
Cuate

## Slide 111: Use our editable graphic resources...
You can easily resize these resources without losing quality. To change the color, just ungroup the resource and click on the object you want to change. Then, click on the paint bucket and select the color you want. Group the resource again when you’re done. You can also look for more infographics on Slidesgo.

## Slide 114
JANUARY
FEBRUARY
MARCH
APRIL
PHASE 1
Task 1
Task 2
JANUARY
FEBRUARY
MARCH
APRIL
MAY
JUNE
PHASE 1
PHASE 2
Task 1
Task 2
Task 1
Task 2

## Slide 117: ...and our sets of editable icons
You can resize these icons without losing quality.
You can change the stroke and fill color; just select the icon and click on the paint bucket/pen.
In Google Slides, you can also use Flaticon’s extension, allowing you to customize and add even more icons.

## Slide 118
Educational Icons
Medical Icons

## Slide 119
Business Icons
Teamwork Icons

## Slide 120
Help & Support Icons
Avatar Icons

## Slide 121
Creative Process Icons
Performing Arts Icons

## Slide 122: Nature Icons

## Slide 123: SEO & Marketing Icons

## Slide 125: Hydro Energy Potential in Ghana - I
Refresher: basic energy and power calculation skills from the previous workbook sessions!
Data Needed:
Current Hydro Power potential: 840 MW
1 MW = 1,000 kW
1 day = 24h
1 year = 365 days
Lets assume that your househhold consumes about 2000 kWh per year.
Question
How many years could you power your home with the additionial energy potential from hydro power? Let‘s first make an estimate, and then work through the calculations together in class to find the answer!
Notes: Source for data: https://www.sciencedirect.com/science/article/abs/pii/S030142152300352X
If

## Slide 126: Hydro Energy Potential in Ghana - II
Hint: Power is the energy produced per second, find the energy produced in 1 year.
Step 1: Total Potential Energy in one year in kWh.
Energy in 1 Hour (Hint do a Conversion from Power to Energy)
  Power = 840 MW = 840,000 kW
  Energy in 1 hour = 840,000 kW × 1 hour = 840,000 kWh
Energy in 1 Day?!
  1 Day = 24 hours
  840,000 kWh * 24 hours/day = 20,160,000 kWh/day
Energy in 1 year
  1 year = 365 days
  20,160,000 kWh/day * 365 days/year = 7,358,400,00 kWh/year

## Slide 127: Hydro Energy Potential in Ghana - III
Total Energy in one year = 7,358,400,00 kWh/year
Step 2: Your energy consumption in one year = 2,000 kWh/year
Step 3: How many years one household can be powered?
Total Energy in one year / Energy consumption household in one year
= 7,358,400,00 kWh/year / 2,000 kWh/year
= 3,679,200 years
Your family would never have to worry about energy for a very long time!